## Slide 1: Geo-X training course
Lesson 3: Data inputs
Notes: Welcome to Lesson 3 of the Geo-X training course: Data Inputs. In the previous lesson, you installed Geo-X, set up your environment, and established a Git workflow. Now we turn to what the model actually needs before it can run. This lesson is the most data-intensive of the six – but we have structured it so that you come away with a clear mental map of what each input is, where it comes from, and how to configure it for your own case study. By the end, you will be ready to run the model in Lesson 4.

## Slide 2: Learning outcomes
By the end of this lesson, you will:
Understand the three types of input data Geo-X requires: Spatial hexagons, techno-economic parameters, and the configuration file.
Define demand locations correctly.
Understand production pathways for hydrogen and ammonia and how they map to Geo-X’s parameter structure.
Recognise which parameter files and config.yaml settings control the modelling choices in Geo-X.
2
Notes: Here are the four things you should be able to do by the end of this lesson. First, understand the three types of input data Geo-X requires: spatial hexagons, techno-economic parameter files, and the configuration file. Second, define demand locations correctly – this is one of the most consequential analytical decisions you will make when applying Geo-X. Third, understand the production pathways for hydrogen and ammonia and how they map to the parameter file structure. And fourth, recognise the technical alternatives available in Geo-X, such as demand flexibility, and know which parameters control them. More advanced alternatives, including power purchase agreements and salt cavern storage, are covered in Lesson 6.

## Slide 3
Overview: the three input types
What Geo-X needs to run
Production pathways and their parameters
Techno-economic parameters
Checklist and wrap-up
Geo-X-data-prep: what it does and how it flows
Table of contents
Notes: Here is the structure of this lesson. We start with an overview of the three input types – what Geo-X needs before it can run. We then look at the data preparation pipeline that produces the spatial hexagon files. From there we move into the production pathways for hydrogen and ammonia, followed by the techno-economic parameter files in detail – including demand parameters and the configuration file. We close with a pre-run checklist and a preview of Lesson 4.​

## Slide 4: What Geo-X needs to run
Geo-X
Optimisation model runs and produces outputs
Spatial hexagons
Geographic units covering the study area (e.g., country)
Parameter files
Techno-economic assumptions: costs, efficiencies, capacities, etc.
config.yaml
Instructions for Geo-X about what to run
Notes: Before Geo-X can run, three things must be in place. The first is spatial hexagons – geographic units that tile the study area, typically a country, into a regular grid. Each hexagon represents a potential production site and carries spatial attributes like solar resource quality, wind resource, and distance to roads and water. The second is a set of parameter files – the techno-economic assumptions that define costs, efficiencies, and capacities for every component in the production and transport chain. The third is the configuration file – config.yaml – which tells Geo-X what to run: which country, which commodity, which year of weather data, which solver, and which transport options to consider. All three must be correctly in place before Snakemake can execute the model. This slide is the map for the lesson – everything that follows fills in these three boxes.

## Slide 5: Geo-X-data-prep: What it does and how it flows
Geo-X-data-prep creates a spatial hexagon file containing the available land per hexagon.
Exclusion criteria are given by:
prep_before_spider.py
Raw inputs
Natural Earth
OSM/ Geofabrik
Copernicus Land Cover
HydroSHEDS
Marine Regions
Applies GLAES exclusions
Outputs eligible land rasters.
SPIDER
Hexagon tiling engine:
Divides land into H3 hexagonal cells.
Assign eligible area per hexagon.
Uses country config.yaml for parameters.
prep_after_spider.py
Finalises hex file
Merges SPIDER + GLAES outputs
Assigns country to hexagons
Correct CRS
Writes output
Geo-X
More details can be found in the README of the Geo-X and Geo-X-data-prep repositories.
hex_final_[ISO].geojson
Slope
Steep terrain excluded
Water bodies
Rivers, lakes, distance buffers
Land cover
Forest, urban, croplands
Distance constraints
Roads, infrastructure buffers
Geo-X-data-prep creates the spatial hexagons in these 3 steps:
Notes: The spatial hexagon file does not come from Geo-X itself – it is produced by a companion repository called Geo-X-data-prep. Understanding what this pipeline does and what it produces is important, even if you are using pre-built hexagon files for your first runs. The pipeline works in three stages. First, a script called prep_before_spider.py collects raw spatial data from five sources – Natural Earth for administrative boundaries, OpenStreetMap via Geofabrik for roads, Copernicus for land cover, HydroSHEDS for river and water body data, and Marine Regions for coastal boundaries. It then applies GLAES land exclusion criteria to remove areas that are unsuitable for production. There are four main exclusion categories: slope – steep terrain is excluded because it is unsuitable for solar panels and wind turbines and makes construction impractical; water bodies – rivers, lakes, and coastal areas are excluded along with distance buffers around them; land cover – forests, urban areas, and croplands are excluded based on the Copernicus classification; and distance constraints – areas that are too far from roads or water infrastructure are excluded because access costs become prohibitive. The second stage is SPIDER, which divides the remaining eligible land into H3 hexagonal cells and assigns the eligible area and spatial attributes to each hexagon. The third stage is prep_after_spider.py, which merges the SPIDER output with the GLAES results, assigns the correct country identifier, fixes the coordinate reference system, and writes the final output: hex_final followed by the ISO country code, in GeoJSON format. That file is what goes into the data folder of your Geo-X repository. Full documentation for running this pipeline on a new country is in the README files of both repositories and in the hands-on document for this lesson.

## Slide 6
Overview: the three input types
Understanding modelling before parameters
Production pathways and their parameters
Techno-economic parameters
Checklist and wrap-up
Hydrogen and ammonia pathways
Table of contents
Notes: We now move into the second section of this lesson: production pathways and their parameters. Before you can configure Geo-X correctly, you need to understand what the model is actually doing – what components it is optimising, how they connect to each other, and what parameters control each one. The next two slides present the basic modelling architecture for hydrogen and ammonia. More advanced configurations, including demand-side flexibility, power purchase agreements, and salt cavern storage, are covered in Lesson 6.​

## Slide 7: Understanding modelling before parameters
The relevance of knowing the model
To configure Geo-X correctly, it is relevant to understand what the model is doing.
Each modelled device is characterised by techno-economic parameters
Each element requires the investment cost, efficiencies, and capacities.
Next slides present basic modelling over which you can customise
More specific alternatives will be explored in Lesson 6.
Carrier | Components
Electricity | Solar photovoltaics, onshore wind, geothermal, PPA legacy installation, batteries.
Hydrogen | Hydrogen storage, salt caverns, demand (flexible-inflexible).
Ammonia | Ammonia storage, salt caverns, demand.
Conversion | Electrolysers, Haber-Bosch, fuel cell.
Transport | Pipeline or road transport (trucking).
Notes: This slide gives you the conceptual framework before we look at the specific pathway diagrams. Every device in Geo-X – a solar panel, an electrolyser, a storage tank – is characterised by a set of techno-economic parameters: its investment cost, its operational cost, its efficiency, and its capacity bounds. The model optimises the combination of these devices at each hexagon location to minimise the total levelised cost of delivering the commodity to the demand point. The table on this slide shows how Geo-X groups components by energy carrier. Electricity carriers include solar photovoltaics, onshore wind, geothermal, batteries, and, in some configurations, a generic generator representing a power purchase agreement or legacy installation. Hydrogen carriers include hydrogen storage and the demand component, which can be flexible or inflexible. Ammonia carriers include ammonia storage and ammonia demand. Conversion components include electrolysers, the Haber-Bosch synthesis unit, and fuel cells. Transport covers both pipeline and road trucking options. Each of these maps directly to one or more files in the parameter folder structure, which we will look at in the next section.

## Slide 8: Hydrogen pathways
 | Electricity
 | Hydrogen
 | Conversion
 | Renewable source
Electrolyser
Onshore wind
Solar
Battery
Compressed hydrogen storage
Transport
Inflexible hydrogen demand
C
C
The flowchart presents the basic modelling of hydrogen production based on electrolysers. Colours represent different energy carriers.
A sophisticated model involves additional devices that will be explored in Lesson 6.
Notes: This diagram shows the basic hydrogen production pathway as modelled in Geo-X. Follow the colours: renewable electricity, shown in yellow, is generated by solar photovoltaics and onshore wind. That electricity can be stored in batteries or passed directly to the electrolyser, shown in the conversion layer. The electrolyser produces hydrogen, which can be stored in a compressed hydrogen tank or transported directly. Transport to the demand point can be via truck or pipeline, depending on the configuration you set in config.yaml. At the demand end sits the hydrogen demand node, which in the basic model is inflexible – meaning the model must supply a constant volume at every time step. Notice the letter C transport nodes – this indicates conversion steps to facilitate the transport (for instance, in some cases, transporting hydrogen in ammonia form can be efficient). The key point for configuration: every box in this diagram corresponds to parameters you will set in the files we discuss shortly. If you understand the pathway, you understand why each parameter file exists.

## Slide 9: Ammonia pathways
Electrolyser
Onshore wind
Solar
Battery
Compressed hydrogen storage
Haber-Bosch
Fuel cell
Ammonia storage
Ammonia demand
 | Electricity
 | Hydrogen
 | Ammonia
 | Conversion
 | Renewable source
Transport
C
C
Ammonia pathways involve the interaction of 3 pathways (electricity, hydrogen, and ammonia), and therefore, their modelling is more complex.
Notes: The ammonia pathway builds directly on hydrogen. Everything in the hydrogen pathway is still present – renewables, batteries, electrolyser, hydrogen storage. But two additional components appear. The first is an air separation unit, which produces the nitrogen that Haber-Bosch synthesis requires. The second is the Haber-Bosch reactor itself, which combines hydrogen and nitrogen to produce ammonia. Ammonia is then stored – in this basic model as a pressurised tank – and transported by truck to the ammonia demand node. Notice also the fuel cell: this allows ammonia to be converted back to electricity if needed for the production process. The ammonia pathway therefore involves three interacting energy carriers – electricity, hydrogen, and ammonia – which makes its optimisation more complex than hydrogen alone. In practice this means ammonia runs take somewhat longer to compute, and the parameter file structure is also more extensive. The key advantage of ammonia over hydrogen is transport efficiency: ammonia is liquid at moderate pressure, making it significantly cheaper to move over long distances, which is why it often wins in export-oriented scenarios.

## Slide 10
Overview: the three input types
Parameter file structure
Production pathways and their parameters
Techno-economic parameters
Checklist and wrap-up
Where do parameters come from?
Demand parameters
Config.yaml: the scenario dial
Table of contents
Notes: We now move into the techno-economic parameter section – the practical core of this lesson. We will look at the full parameter file structure, discuss where parameter values come from, examine the demand parameters in detail, and walk through the configuration file. By the end of this section, you will know exactly what to open, what to change, and why – before running Geo-X for the first time.​

## Slide 11: Parameter file structure
Parameters folder
basic_[commodity]_plant
buses.csv
generators.csv
links.csv
storage_units.csv
stores.csv
Country [ISO]
transport_parameters.xlsx
technology_parameters.xlsx
pipeline_parameters.xlsx
demand_parameters.xlsx
country_parameters.xlsx
conversion_parameters.xlsx
[commodity]
File | Controls
Buses.csv | The types of energy carriers (e.g.,electricity, ammonia, hydrogen)
Generators.csv | Technology options, costs, efficiency
Links.csv | Technology options for energy conversion (e.g., electrolysers), costs, efficiency
Storage_units.csv | Storage technologies in power capacity (e.g., hydrogen compressor)
Stores.csv | Storage technologies in energy capacity (e.g., compressed hydrogen tank)
Transport_parameters.xlsx | Trucking transport costs and parameters (e.g., average speed)
Technology_parameters.xlsx | Grid and water costs
Pipeline_parameters.xlsx | Pipelines costs and parameters (e.g., CAPEX,OPEX)
Demand_parameters.xlsx | Demand location, volume, commodity state
Country_parameters.xlsx | Interest rate, water cost, country level assumptions
Conversion_parameters.xlsx | Conversion of commodity for transport purposes
This structure is used for both ammonia and hydrogen commodities.
The basic_[commodity]_plant folder contains all modelling components related to commodity production at a specific location.
The Country/commodity folder manages transport from the production location to the demand location.
Notes: The parameters folder in your Geo-X repository contains two levels of files. The first level is the basic plant folder – named basic_hydrogen_plant or basic_ammonia_plant – which contains the component-level files for production at a single location. These are CSV files: buses.csv defines the energy carriers; generators.csv defines renewable generation technologies with their costs and efficiencies; links.csv defines conversion technologies like the electrolyser and Haber-Bosch unit; storage_units.csv covers storage measured in power capacity such as the hydrogen compressor; and stores.csv covers storage measured in energy capacity such as the compressed hydrogen tank. The second level is the country and commodity folder, which contains spreadsheet files for transport and country-level parameters. Transport_parameters.xlsx covers trucking costs and logistics. Pipeline_parameters.xlsx covers pipeline capital and operating costs. Demand parameters.xlsx – which we will look at in the next slide – defines the demand point. Country_parameters.xlsx sets the interest rate, water costs, and other country-level assumptions. Conversion_parameters.xlsx handles commodity conversion for transport, such as the energy cost of liquefying hydrogen. Technology_parameters.xlsx covers grid and water infrastructure costs. This structure is identical for both hydrogen and ammonia – only the values differ. When you apply Geo-X to a new country or commodity, the task is to populate these files with values appropriate to your context.

## Slide 12: Where do parameters come from?
Parameters are your assumptions.
Geo-X does not prescribe values; it will analyse whatever you give it.
Default values are a starting point
The files with Geo-X contain example values
Output quality depends on input quality
Poor inputs → poor outputs
Uncertainty to be explored
Geo-X is built to run scenarios, allowing sensitivity analysis
In Lessons 5 and 6, we will explore alternatives for sensitivity analysis.
Notes: A question that always comes up at this point is: where do the parameter values actually come from? The honest answer is that they are your assumptions – Geo-X does not prescribe values, it will analyse whatever you give it. The files in the repository contain example values drawn from published sources, primarily IRENA's Renewable Power Generation Costs report for solar and wind capital costs, IEA's Hydrogen and Ammonia Technology Roadmaps for electrolyser and Haber-Bosch parameters, World Bank data for country-level cost of capital, and academic literature for transport costs. These are a starting point – not ground truth. The quality of your outputs depends directly on the quality of your inputs. This is not a weakness of Geo-X; it is how all techno-economic models work. The appropriate response is to treat parameters as assumptions, run multiple scenarios to test sensitivity, and be transparent about your sources when reporting results. Lessons 5 and 6 will show you how to structure that kind of sensitivity analysis systematically.

## Slide 13: Demand parameters define the geography of the analysis
For basic models the demand is inflexible: constant demand over the year
Demand point
(lat,lon)
Parameter | What it defines
Latitude/longitude | Where in the country the commodity is delivered
Annual_demand | Total volume the model must supply each year
Commodity_state | Physical form at delivery – affects transport options
Choosing the demand point is an analytical decision.
Shipping
Border crossing
Industrial purposes
Notes: The demand parameters file deserves its own slide because it is one of the most consequential input you will change for any new application – it literally defines the geography of the analysis. For every demand centre you want to model, you specify four things. The latitude and longitude define where in the country the commodity is delivered – this could be a port for export, a border crossing, a refinery, or an industrial hub. The annual demand sets the total volume the model must supply over the year, in tonnes. And the commodity state defines the physical form of the commodity at the delivery point – for example, gaseous hydrogen, liquid hydrogen, or ammonia – which determines what transport options are available. In the basic model, demand is inflexible: the model must supply a constant rate at every time step throughout the year. Choosing the demand point is a genuine analytical decision, not a technical one. A port location gives you an export cost curve. A border crossing gives you a transit cost estimate. An inland industrial cluster gives you a domestic supply cost. Each tells a different policy story, and the choice should be driven by the question you are trying to answer.

## Slide 14: Config.yaml: the scenario dial
config.yaml
01
scenario:
02
country: ['UA']
03
weather_year: [2023]
04
plant_type: 'ammonia'
05
years_to_check: 1
06
freq: '1H'
07
generators_dict:
08
{'solar':[], 'wind':[]}
09
panel: 'CSi'
10
turbine: 'NREL_Ref...'
11
gen_capacity: s:1 / w:4
12
generic_generator:
13
marginal_cost: 100
14
solver: 'gurobi'
15
transport:
16
pipeline_construction: True
17
road_construction: True
18
currency: 'euros'
19
h2_demand_flex: False
■ edit before each run
■ advanced / rarely changed
country
ISO code of the study country
weather_year
Year of climate data for solar and wind capacity factors
plant_type
'hydrogen' or 'ammonia' — determines pathway and parameter folder
generators_dict
Which renewables to include, in this example, wind and solar
solver
'gurobi' or 'cbc' — must match your installed solver (see Lesson 2)
transport
Toggle pipeline_construction and road_construction True/False per scenario
Notes: The configuration file – config.yaml – is the master switch for every model run. Before you execute Snakemake, you review this file and set it for your scenario. The fields highlighted in dark blue are the ones you will edit most frequently. Country takes the ISO two-letter code of your study country – UA for Ukraine, NA for Namibia, and so on. Weather year selects the year of ERA5 climate data used to generate solar and wind capacity factors. Plant type is either hydrogen or ammonia, and must match the parameter folder you have set up. Generators dict specifies which renewable technologies to include in the optimisation – in the example shown, solar and wind are both active. Solver must match what you installed in Lesson 2 – either cbc or gurobi. And the transport switches – pipeline construction and road construction – allow you to turn on or off specific transport options for each scenario, which is useful for comparing infrastructure investment choices. The fields in lighter blue are more advanced settings that you will rarely need to change, but they are documented in the README for reference. The key habit is: before every run, open config.yaml and confirm these six settings are correct for the scenario you intend to run.

## Slide 15
Overview: the three input types
Are your inputs ready?
Production pathways and their parameters
Techno-economic parameters
Checklist and wrap-up
Table of contents
Notes: We are now in the final section of this lesson. Let us check whether your inputs are ready and preview what is coming in Lesson 4.​

## Slide 16: Are your inputs ready?
Spatial hexagons
hex_final_[ISO].geojson
File copied into Geo-X folder.
Modelling understanding
Pathway defined (hydrogen, ammonia, or others). Components and structure.
Demand point definition
Lat/Lon, annual volume, commodity state of delivery.
Parameter files update
Generators, storage, country, transport, conversion params, etc.
Config.yaml set
Country, plant type, weather year, solver, transport switches.
Renewable resource data
Solar and wind capacity factors downloaded via CDS API (in Lesson 4).
The last input data is automatically collected through Geo-X. This content is part of Lesson 4.
Notes: Before you run Geo-X for the first time, work through this checklist. First, confirm the hexagon file is in place – hex_final followed by your ISO code, as a GeoJSON file, copied into the data folder of your Geo-X repository. Second, confirm you have a clear understanding of the pathway you are modelling – hydrogen or ammonia – and that the component structure makes sense to you before you try to configure it. Third, define your demand point – latitude, longitude, annual volume, and commodity state – and enter it into demand_parameters.xlsx. Fourth, review and update the parameter files – at minimum generators.csv, country_parameters.xlsx, and the transport parameters – to reflect your context and data sources. Fifth, open config.yaml and confirm country, plant type, weather year, solver, and transport switches are all set correctly for your run. The sixth item – renewable resource data via the CDS API – is handled automatically by Geo-X during the run, and we cover that process in detail in Lesson 4. If the first five items are in place, you are ready.

## Slide 17: Lesson 3 done! What is next:
What you’ve set up so far
Lesson 4 coming up
Geo-X-data-prep pipeline
H2 and NH3 pathways
Parameter file structure
Demand point as analytical decision
Config.yaml as scenario dial
Parameters are your assumptions
Pre-run checklist
With your data in place, you are in a position to run the model.
Weather data download
Snakemake execution pipeline
Reading and interpreting outputs
Well done! See you in Lesson 4.
Note: Figures and graphics throughout this course were produced by the authors, generated either through custom Python code or with the assistance of Claude AI.
Notes: You have now completed Lesson 3. You understand the three input types Geo-X requires, how the data preparation pipeline produces spatial hexagons, what the hydrogen and ammonia production pathways look like and how they map to the parameter files, how to define a demand point as an analytical decision, how to use config.yaml as your scenario dial, and how to verify your inputs with the pre-run checklist. In Lesson 4 we put all of this into action: we will download weather data via the CDS API, execute the Snakemake workflow, and look at how to read and interpret the outputs that come out the other side. Well done – see you in Lesson 4.

## Slide 18: Thank you
www.climatecompatiblegrowth.com
Notes: Thank you for completing Lesson 3 of the Geo-X training course. Your inputs are ready – in Lesson 4 we run the model.