## Slide 1: Geo-X training course
Lesson 5: Interpreting the results
Notes: Welcome to Lesson 5 of the Geo-X training course: Interpreting the Results. In the previous lesson you ran Geo-X end to end and produced your first cost maps and GeoJSON output files. In this lesson we go deeper – learning how to load, inspect, visualise, and analytically interpret those outputs. We will work with cost heatmaps, cost component maps, and build a cumulative supply cost curve. By the end of this lesson, you will be able to move from raw model output to policy-relevant insight.

## Slide 2: Learning outcomes
By the end of this lesson, you will:
Load and inspect Geo-X GeoJSON outputs using Python and geopandas.
Read and interpret heatmaps: Spatial gradients, production zones, dominant cost drivers.
Decompose the levelised cost into its components and identify what drives costs in different regions.
Construct a cumulative supply cost curve from hexagon-level outputs and understand its assumptions and limitations.
2
This lesson uses Python and geopandas for all analysis. The same GeoJSON outputs are fully compatible with R, QGIS, or any GIS tool.
Notes: Here are the four learning outcomes for this lesson, together with an important note on tools. By the end you will be able to load and inspect Geo-X GeoJSON outputs using Python and geopandas; read and interpret cost heatmaps, including their spatial gradients and dominant cost drivers; decompose the levelised cost into its components and explain what drives costs in different regions; and construct a cumulative supply cost curve from hexagon-level outputs, understanding its assumptions and limitations. On the tool choice: this lesson uses Python and geopandas as the primary analysis environment, with Jupyter notebooks as the reference format. However, the same GeoJSON output files are fully compatible with R, QGIS, or any other GIS tool you prefer. If you are more comfortable in one of those environments, the hands-on document includes links to equivalent resources. The code in this lesson is designed to be copied and pasted directly into a notebook – you do not need to write it from scratch.

## Slide 3
Loading and inspecting outputs
Setting up your analysis environment
Reading heatmaps
Cost breakdown analysis
Supply cost curves
Wrap up
First inspection: sanity checks
Table of Contents
Notes: Here is the structure of this lesson. We start with setting up the analysis environment and running the first sanity checks on the output files. We then move into heatmap visualisation – covering the design decisions behind how you plot, then how to read the spatial patterns analytically, including a second geography example. We then look at cost components – how to plot and interpret the breakdown. And we finish with supply cost curves: what they are, how they are constructed, and how to build one in Python. Each section builds directly on the previous one.

## Slide 4: Setting up your analysis environment
4
This lesson uses .ipynb as reference format. But the same code runs in other alternatives.
mamba activate geox
(geox) user@machine:~$
Jupyter notebook
Activate the Geo-X environment
Open Jupyter in your browser
The same code runs in VS Code or plain Python scripts
Analysis.ipynb: copy and paste into your notebook
# ── Cell 1: imports ──────────────────────────────
import geopandas as gpd
import pandas as pd
import matplotlib.pyplot as plt
import matplotlib.colors as mcolors
# ── Cell 2: set your scenario ────────
ISO = "UA"
YEAR = "2023"
TYPE = "hydrogen"
# ── Cell 3: load output files ────────
# total cost file (LCOH / LCOA per hexagon)
df_cost = gpd.read_file(
f"results/hex_total_cost_{ISO}_{YEAR}_{TYPE}.geojson"
)
# cost components file (breakdown per component)
df_comp = gpd.read_file(
f"results/hex_cost_components_{ISO}_{YEAR}_{TYPE}.geojson"
)
# ── Cell 4: quick check ───────────────────────────
print(df_cost.shape)
print(df_cost.columns.tolist())
df_cost[["total_cost","demand_centre","geometry"]].head()
In the terminal:
Notes: Before we start plotting, let us set up the analysis environment. Open a terminal, activate the geox environment using mamba activate geox, and then launch Jupyter notebook from your Geo-X repository directory. The notebook will open in your browser. From there, create a new notebook – or open the Analysis dot ipynb file if one is provided with the course materials. The four code cells on this slide set up everything you need. Cell 1 imports the three libraries we will use throughout: geopandas for spatial data, pandas for tabular operations, and matplotlib for plotting. Cell 2 sets the three scenario variables – ISO country code, weather year, and commodity type – so you only need to change them in one place when you switch scenarios. Cell 3 loads both output files: the total cost file and the cost components file, using the naming convention we covered in Lesson 4. Cell 4 runs a quick check – printing the shape of the data and the first few rows. If this runs without errors, your environment is correctly set up and you are ready to start analysing. Note that the same code runs identically in VS Code or as a plain Python script – Jupyter is just the reference format for this lesson.
Jupyter activation:
mamba activate geox mamba install -c conda-forge jupyterlab jupyter lab

## Slide 5: First inspection: sanity checks
5
Make this a habit before any visualisation: Quick test to catch most problems early.
Shape and head
Question: How many hexagons? How many demand centres?
print(df_cost.shape)
print(df_cost["demand_centre"].unique())
Looks good if:
Rows=hexagons x demand centres
Demand centre lists your locations
Watch out for:
Very few rows: restrict_hexagons may still be True in config.yaml
Wrong demand_centre name: check demand_parameters.xlsx
print(df_cost.columns.tolist())
print(df_comp.columns.tolist())
Looks good if:
df_cost has total_cost, geometry
Df_comp has production_cost, transport_cost, storage_cost.
Watch out for:
Missing columns: rule may not have completed check logs
Unexpected columns: old output file, re-run map_all
Describe
Question: Is the cost range reasonable for this country and commodity?
df_cost[["total_cost"]].describe()
df_cost["total_cost"]
.isnull().sum()
Looks good if:
Mean ~5-15 €/kg for green H2
Watch out for:
Very high values: check demand volume in params.
Many nulls: infeasible hexagons, check exclusion layers
Columns
Question: Are all expected cost fields present?
Notes: Before producing any visualisation, always run these three sanity checks. Think of them as analytical hygiene – a quick test that catches the most common problems early, before you spend time interpreting a map that turns out to have an issue. The first check is shape and head: print the shape of the dataframe and the unique demand centres. The shape tells you how many rows you have – it should be the number of hexagons multiplied by the number of demand centres. If you see very few rows, restrict_hexagons may still be set to True in config.yaml from a test run in Lesson 4. If the demand centre names are wrong or missing, check demand_parameters.xlsx. The second check is columns: print the column names of both files. The total cost file should have total_cost and geometry. The components file should have production_cost, transport_cost, storage_cost, and water_cost. Missing columns usually mean a rule did not complete – check your Snakemake logs and re-run map_all. Unexpected extra columns often indicate you are accidentally loading an old output file from a previous run. The third check is describe: run describe on the total_cost column and count the nulls. For green hydrogen, a mean in the range of five to fifteen euros per kilogram is broadly plausible – though this depends heavily on your country and parameter assumptions. Very high values suggest the demand volume may be unrealistically large. Many nulls indicate infeasible hexagons – check whether your exclusion layers are too aggressive or your demand target is too high for some locations.

## Slide 6
Loading and inspecting outputs
Reading heatmaps
Cost breakdown analysis
Supply cost curves
Wrap up
  Plotting the heatmaps: visualisation choices
  Reading the spatial gradient and its drivers
  Same tool, other geography
  What a heatmap cannot tell you
Table of Contents
Notes: We now move into heatmap visualisation. This section covers both how to produce the maps and how to read them analytically.

## Slide 7: Plotting the heatmaps: visualisation tools
7
# filter one demand centre
df = df_cost[df_cost["demand_centre"] == "Odessa"]
# plot
fig, ax = plt.subplots(figsize=(10, 6))
df.plot(column="total_cost", cmap="viridis_r",legend=True, ax=ax,missing_kwds={"color": "lightgrey"})
plt.title("Odessa — Total LCOH"); plt.show()
Notebook: plot the heatmap
Colour map | Sequential (viridis/plasma) for absolute cost; diverging (RdYlGn) for relative to benchmark
Scale cap | Cap at P95 to avoid outliers dominating vmax=df["total_cost"].quantile(0.95)
Absolute vs relative | Absolute for single scenario. Relative (delta cost) for comparison of scenarios
Null hexagons | missing_kwds={"color":"lightgrey"} Makes excluded areas visible rather than blank
Static vs interactive | PNG for reports, folium/plotly for web embedding and hover inspection
Odessa
What this map shows:
🟡 Yellow (south): lowest cost, near Odessa
🟢 Green (centre): mid-range, good renewables
🟣 Purple (west): highest cost, mountainous
–> Explanations behind the heatmaps depend on the context of the country. A good exercise is to find explanations for what you see.
Design decision
Notes: This slide covers the visualisation design decisions you will face when plotting heatmaps – and there are more of them than you might expect. The code on the left produces the basic map: filter to a single demand centre, call dot-plot with a column, colour map, and legend, and handle null hexagons with a grey fill using missing_kwds. But the five design decisions on the right are where the analytical choices live. The first is colour map: sequential colour maps like viridis or plasma work well for absolute cost – they show low cost at one end and high cost at the other. Diverging maps like red-yellow-green work better when you are plotting cost relative to a benchmark – for example, which hexagons are above or below a reference price. The second decision is scale capping: by default matplotlib stretches the colour scale to the full data range, which means a small number of very expensive outlier hexagons can wash out the variation in the main part of the country. Capping at the 95th percentile using vmax makes the map much more informative. Third, decide whether you want to show absolute cost or a relative delta from a baseline scenario – the latter is more useful for scenario comparison. Fourth, handle null hexagons explicitly: using missing_kwds with a light grey colour makes excluded land visible, which is analytically important – you want to see where the model chose not to optimise. And fifth, decide between static PNG output for reports and presentations, or an interactive map using folium or plotly for exploratory analysis where you want to hover and inspect individual hexagons. There is no single right answer – the choice depends on the question and the audience.

## Slide 8: Reading the spatial gradient
Odessa
Odessa
Odessa
Odessa
Heatmaps can inform “visual correlations”:
Low LCOH goes with low installed capacity: a strong resource needs less capacity to meet the same demand.
Solar and wind capacity are often anti-correlated: where one is strong, the other tends to be weaker.
Solar-heavy hexagons require more battery storage to smooth intermittent output and maintain continuous H₂ production.
–> Given the cost drivers, how to know the relevance of every cost structure?
Notes: Now that we know how to produce the map, let us focus on how to read it. The most important analytical habit when working with Geo-X heatmaps is to look at multiple maps together rather than the total cost map in isolation. The reason is that the total cost heatmap shows you where production is cheap, but not why. The four maps on this slide – total cost, solar potential, wind potential, and storage cost – tell a much richer story together. The first observation is that LCOH and LCOA heatmaps usually show similar spatial patterns to the solar and wind capacity factor maps. Where renewable resources are strongest, production costs are lowest – because less installed capacity is needed to meet the same annual demand. This correlation is strong and reliable: it is almost always the first thing to check when you see an unexpectedly cheap or expensive region. The second observation is more subtle. Solar and wind potential are often anti-correlated spatially – regions with excellent solar irradiation tend to have weaker wind, and vice versa. The model exploits complementarity where it exists, but regions that rely heavily on a single source tend to see higher storage costs. This leads to the third observation: storage cost is inversely correlated with resource consistency, not just resource quality. A location with strong average solar but high day-to-night variability – such as a desert location with clear skies but no wind – requires more battery storage to maintain continuous hydrogen production throughout the year. This is why two hexagons with similar average capacity factors can have meaningfully different total costs: one has consistent output, the other needs a large storage buffer to smooth the peaks. Understanding these correlations is what allows you to move from reading the cost map to explaining it.

## Slide 9: Different geography
Different numbers, but why?
Is it the renewable resource quality?
Ghana has strong solar irradiation but weaker wind.
Is it the cost of capital?
Financing costs reflect investment risk and macroeconomic conditions.
Is it the supply chain effects on CAPEX/OPEX?
Equipment costs vary between regions.
Is it the infrastructure availability?
Road networks, water access, and port proximity affect transport and water costs.
Ghana – Total LCOH
Same workflow, entirely different resource and infrastructure context: Are those results directly comparable?
Before comparing two countries, we recommend being explicit about:
Which parameters differ.
Whether they reflect real-world variation or modelling assumptions.
Notes: This slide introduces a second geography – Ghana – to demonstrate that the Geo-X workflow is fully transferable across very different regional contexts. The workflow is identical: the same Python code, the same Snakemake pipeline, the same output file structure. But the results tell a different story, shaped by Ghana's specific resource profile, infrastructure context, and economic conditions. However, before drawing any conclusions from the comparison, a good modeller needs to ask a more fundamental question: are these two results actually comparable, and if so, on what basis? When you see different LCOH numbers between Ukraine and Ghana, several things could be driving that difference. It could be the renewable resource quality – Ghana has strong solar irradiation but generally weaker wind than parts of Ukraine. It could be the cost of capital – financing costs reflect investment risk and macroeconomic conditions, which differ significantly between the two countries. It could be supply chain effects on CAPEX and OPEX – equipment costs and installation costs vary between regions. Or it could be infrastructure availability – road networks, water access, and port proximity all affect transport and water costs. Geo-X can directly support this kind of trade-off analysis. A country with a stronger investment environment but comparatively weaker renewable resources can be explicitly compared against a country with excellent resources but higher financing costs – and the tool makes those trade-offs quantifiable and transparent. But the key discipline is to be explicit, before interpreting any cross-country comparison, about which parameters differ between the two runs, and whether those differences reflect real-world variation or modelling assumptions. Conflating the two leads to misleading conclusions.

## Slide 10: What the heatmap cannot tell you
10
What it cannot tell you and what to do
Production volume potential per location
The map shows unit cost, not how much a hexagon could produce at that cost. Low LCOH is not the same as large supply potential.
Suggestion: Build a supply curve (next in this lesson).
Sensitivity to demand centre placement
Moving the demand point changes every hexagon transport cost, and the whole map shifts.
Suggestion: Run alternative demand locations (Lesson 4).
Parameter sensitivity
The map reflects your assumptions: electrolyser CAPEX, interest rate, water costs. Change the assumptions, the map changes.
Suggestion: Run sensitivity scenarios.
Multi-year weather variability
One weather year may be atypically good or bad for solar and wind. A single year may not be a robust estimate.
Suggestion: Run multiple weather years.
Columns
For each hexagon and for each demand centre:
Levelised cost of delivered commodity
Cost breakdown by component
Optimal capacity mix
Spatial pattern across the country
One run = one snapshot
Fixed parameters.
The map is a single answer, not a full picture.
Notes: This slide makes an important point about the limits of heatmap analysis – and it is worth dwelling on, because it is easy to over-interpret a single cost map. The heatmap tells you, for each hexagon and each demand centre, the levelised cost of delivered commodity, the cost breakdown by component, the optimal capacity mix, and the spatial pattern across the country. These are genuinely useful outputs. But there are four things the heatmap cannot tell you. First, it does not tell you how much a hexagon could actually produce – it shows unit cost, not supply volume. A low LCOH hexagon with very little eligible land is not the same as a low LCOH hexagon with large eligible area. The supply curve, which we build later in this lesson, addresses this directly. Second, it does not tell you how the results change if you move the demand centre. Every hexagon's transport cost is calculated relative to the current demand point – move it and the whole map shifts. Running alternative demand locations, as covered in Lesson 4, is the appropriate response. Third, the map reflects your parameter assumptions – electrolyser CAPEX, interest rate, water costs. Change the assumptions and the map changes. Sensitivity scenarios are the tool for understanding how robust the results are. And fourth, a single weather year may be atypically good or bad for solar and wind. A single run is a snapshot, not a robust estimate. Running multiple weather years and comparing the curves is good modelling practice. The takeaway: one run is one answer under one set of assumptions. It is the starting point for analysis, not the conclusion.

## Slide 11
Loading and inspecting outputs
Reading heatmaps
Cost breakdown analysis
Supply cost curves
Wrap up
  Plotting cost components
  Interpreting the components maps
  Cost breakdown as a bar chart
Table of Contents
Notes: We now move into cost component analysis — how to break the total levelised cost down into its constituent parts and what each component tells you analytically.

## Slide 12: Plotting cost components
notebook — 2×2 component map (copy and paste)
# ── define components to plot ────────────────
components = [
("production_cost", "Production cost", "viridis"),
("transport_cost", "Transport cost", "plasma"),
("storage_cost", "Storage cost", "magma"),
("water_cost", "Water cost", "cividis"),
]
# ── filter demand centre ──────────────────────
dc = "Odessa"
df = df_comp[df_comp["demand_centre"] == dc]
# ── 2×2 subplot ───────────────────────────────
fig, axes = plt.subplots(2, 2, figsize=(14, 10))
axes = axes.flatten()
for ax, (col, title, cmap) in zip(axes, components):
df.plot(
column=col,
cmap=cmap,
legend=True,
ax=ax,
missing_kwds={"color": "lightgrey"},
vmax=df[col].quantile(0.95), # cap at P95
)
ax.set_title(title, fontsize=12, fontweight="bold")
ax.axis("off")
fig.suptitle(
f"Cost components — {dc} · hydrogen · 2023",
fontsize=14, fontweight="bold"
)
plt.tight_layout()
plt.savefig(f"plots/components_{dc}.png", dpi=150)
plt.show()
Correlated with solar/wind resource
Radial pattern from Odessa
Higher where solar is intermittent
Water costs driven by proximity to ocean or fresh water
Notes: This slide shows how to produce a two-by-two grid of component cost maps. The code structure is clean and reusable: define a list of tuples containing the column name, plot title, and colour map for each component; filter to your demand centre; then loop over the four panels using zip. Each panel uses a P95 cap on the colour scale to prevent outliers from dominating. The four components shown are production cost, transport cost, storage cost, and water cost. Even before interpreting the maps in detail, a few spatial patterns are immediately visible. Production cost follows the renewable resource distribution – it is correlated with the solar and wind maps from slide 8. Transport cost shows a radial pattern centred on Odessa – it rises smoothly with distance from the demand point. Storage cost is higher where solar is most intermittent – as discussed on slide 8, this is the variability effect rather than purely the resource quality effect. And water cost is driven by proximity to ocean or fresh water sources – it tends to be low near the coast and rises inland, with the gradient depending on whether freshwater or seawater treatment is used. Each of these patterns is worth examining before moving to the summary statistics, because the map tells you where each cost driver is important – which is more useful than a single average number.

## Slide 13: Interpreting the component maps
Component | Spatial pattern | What drives it | Analytical question it enables
Production costs | Mirrors renewable resource distribution – lower where solar irradiation or wind capacity factors are strongest. | Solar/wind capacity factors from weather data + optimal technology mix. Less installed capacity needed = lower CAPEX. | Where should production be sited to minimise generation cost? → overlay with exclusion zones
Transport cost | Broadly radial around the demand centre – cost rises with distance from the delivery point. | Road network, truck speed and capacity, distance to demand point. Pipeline toggle changes the shape significantly. | Where does pipeline investment break even vs trucking? → compare pipeline: True vs False
Storage cost | Inversely correlated with resource consistency – not just quality. Variable solar output requires more buffer. | Seasonal variability of solar/wind. Strong summer peaks with weak winter output need storage to maintain year-round production. | Why do two sites with similar avg. capacity factors have different total costs? → compare storage share of LCOH
Water cost | Distance from water bodies – gradient from coast/rivers inland. Often flat in water-rich countries. | Freshwater vs ocean water cost parameters. Most significant in arid regions (MENA, Sahel, etc.). | How much does water scarcity add to LCOH in arid countries? → compare ocean vs freshwater params
The analytical move: from "where is it cheap" → "why is it cheap"
Reading one map in isolation misses the story.
The cost structure, the relative weight of each component, is what tells you why a location is competitive.
Notes: This table brings together the interpretation of all four component maps into a structured analytical framework. Let us go through each component. Production cost mirrors the renewable resource distribution – lower where solar irradiation or wind capacity factors are strongest, because less installed capacity is needed to meet the same annual demand. The analytical question it enables is: where should production be sited to minimise generation cost? This is answered by overlaying the production cost map with the land exclusion zones. Transport cost shows a broadly radial pattern around the demand centre – cost rises with distance from the delivery point, shaped by the road network and truck capacities. The key analytical question is where pipeline investment breaks even versus trucking, which you explore by comparing runs with pipeline_construction set to True versus False. Storage cost is inversely correlated with resource consistency rather than just resource quality – this is the nuance introduced on slide 8. Seasonal variability drives the storage requirement: strong summer solar peaks with weak winter output require large storage buffers to maintain year-round production. The analytical question is why two sites with similar average capacity factors can have different total costs – the answer lies in comparing their storage share of LCOH. Water cost is driven by distance from water bodies and shows a gradient from coast or rivers inland. It is most significant in arid regions. The key question is how much water scarcity adds to LCOH, which you explore by comparing ocean versus freshwater parameter settings. The overarching message of this table is the analytical move from where is it cheap to why is it cheap. Reading the total cost map in isolation misses the story. The cost structure – the relative weight of each component – is what tells you why a location is competitive and what would need to change to make it more or less so.

## Slide 14: Plotting cost components
notebook — stacked bar chart (copy and paste)
# ── define cost columns (water_cost excluded) ──
cost_cols = [
"storage_cost",
"solar_cost",
"wind_cost",
"electrolyser_cost",
"transport_cost",
]
colours = {
"storage_cost": "#E8A0A0", # pink
"solar_cost": "#F5C842", # yellow
"wind_cost": "#A8C4E8", # blue
"electrolyser_cost":"#4CBB8A", # green
"transport_cost": "#BBBBBB", # grey
}
# ── filter to lowest-cost 5% of hexagons ─────
dc = "Odessa"
df = df_comp[df_comp["demand_centre"] == dc]
p05 = df["total_cost"].quantile(0.05)
low = df[df["total_cost"] <= p05]
# ── compute mean per component ────────────────
means = low[cost_cols].mean()
# ── plot ──────────────────────────────────────
fig, ax = plt.subplots(figsize=(6, 7))
bottom = 0
for col in cost_cols:
ax.bar(
"Lowest-cost\n5%",
means[col],
bottom=bottom,
color=colours[col],
label=col.replace("_cost", "").title(),
edgecolor="white", linewidth=0.5,
)
bottom += means[col]
ax.set_ylabel("Average cost by component [€/kg]")
ax.set_title(f"Cost composition — {dc} · hydrogen")
ax.legend(loc="upper right", fontsize=9)
plt.tight_layout()
plt.savefig(f"plots/bar_components_{dc}.png", dpi=150)
plt.show()
In the example, around 25% of the components shown are associated with storage facilities. Can you give an explanation for it?
–> Solar resources are variable daily and seasonally. To maintain continuous H₂ production during the year, the model sizes battery storage to bridge that daily gap.
Notes: This slide introduces the stacked bar chart as a complement to the spatial maps. Where the component maps show you spatial variation across hexagons, the stacked bar gives you an aggregate summary – the average cost composition for a selected subset of hexagons. The code here computes the mean of each cost component for the lowest-cost five percent of hexagons – those at the bottom of the supply curve – and plots them as a stacked bar. This is a useful summary for policy communication: it tells you, for the most competitive production zone, how much of the total cost comes from each component. The example in the slide shows that roughly twenty-five percent of the total cost is associated with storage. This is a meaningful number, and it invites the analytical question: why is storage such a significant share here? The answer connects back to slide 8 and slide 13. Ukraine's most competitive hydrogen production zones rely heavily on solar photovoltaics. Solar output is highly variable – strong during daylight hours and across summer months, absent at night and lower in winter. To maintain continuous hydrogen production throughout the year, the model sizes battery storage to bridge that daily and seasonal gap. The storage cost reflects the capital investment in that buffer capacity. This is a good example of how the stacked bar chart, combined with the spatial maps, tells a coherent analytical story rather than just reporting numbers.

## Slide 15
Loading and inspecting outputs
Reading heatmaps
Cost breakdown analysis
Supply cost curves
Wrap up
  What is a supply cost curve and why does it matter?
  Methodology and assumptions
  Building the supply curve in Python
Table of Contents
Notes: We now move into the final section of this lesson: supply cost curves. This is the output format that most directly connects Geo-X results to policy and investment questions.

## Slide 16: What is a supply cost curve? And why does it matter?
16
Schematic supply cost curve
Cumulative production potential →
your price
reference
competitive at this price →
min
max
A supply cost curve:
Ranks all production hexagons by delivered costs
Assigns each hexagon a production volume
Plots cumulative volume against unit costs
The result is a step curve. Each step is one hexagon, whose width is the production volume and height the cost.
Heatmaps show where it is cheap. The supply curve shows how much is available at each cost level.
Policy questions it answers
How much could this country produce at or below a given cost?
What is the marginal cost of expanding supply?
How does the curve shift when parameters change?
Which locations should be prioritised for first investments?
Notes: A supply cost curve is a standard analytical tool in energy economics, and it is worth understanding clearly what it represents before building one. The curve ranks all potential production locations by their delivered cost and plots cumulative production potential on the horizontal axis against unit cost on the vertical axis. The result is a step function – each step corresponds to one hexagon, whose width represents how much that hexagon could produce and whose height is the cost at which it could produce it. Reading from left to right, the curve moves from the cheapest and most accessible production zones toward the more expensive and marginal ones. This is a fundamentally different kind of output from the heatmap. The heatmap shows where production is cheap. The supply curve shows how much is available at each cost level – which is the question that matters for investment planning and policy design. A supply curve enables four key policy questions. How much of this country's potential is competitive at or below a given cost? What is the marginal cost of scaling up supply beyond the cheapest zones? How does the competitive volume change when parameters like the cost of capital or electrolyser costs shift? And which locations should be prioritised for first investments – those at the flat, low-cost left end of the curve? The horizontal reference price line, which you can set in the code, is where you make the connection to market conditions explicit. Set it at the price of competing fuels, at an import benchmark, or at a policy target, and the curve immediately tells you how much of the country's potential is commercially viable at that price.

## Slide 17: Methodology and assumptions
17
Hexagon grid resolution: Each hexagon covers a determined area. The country is divided into cells with equal demand. H3 resolution 5, ~250 km² per hexagon.
The demand is supplied subject to the land fraction. Eventually, the demand could exceed the potential of the hexagon. The optimisation returns null, and the hexagon is excluded from the supply curve.
Sort and accumulate Sort hexagons by total delivered cost (ascending). Accumulate production potential left to right.
Hexagons are independent plants. The model treats each hexagon as a standalone production site. There is no system interaction.
Demand is fixed per hexagon Each hexagon is sized to meet a fixed annual demand target. This is a screening assumption, not a dispatch-optimised system where demand can be met from multiple locations.
The result is informative and aligned with policy-oriented models. More sophisticated approaches exists (e.g. higher resolution, dynamic capacity scaling, system integration).
How is the curve constructed?
What are the caveats?
Notes: This slide covers the methodology behind the supply curve – how it is constructed from Geo-X outputs and what assumptions are embedded in that construction. Understanding the methodology is essential for interpreting the curve correctly and communicating its limitations honestly. The hexagon grid divides the country into cells at H3 resolution 5, where each hexagon covers roughly two hundred and fifty square kilometres. Within each hexagon, the eligible land fraction – after applying all the exclusion criteria from the data preparation pipeline – determines how much area is available for plant installation. The demand that each hexagon is sized to meet is fixed: it is the value specified in demand_parameters.xlsx. If the eligible area within a hexagon is insufficient to meet that demand, the optimisation returns null and the hexagon is excluded from the supply curve. The supply curve is then constructed by sorting hexagons from lowest to highest delivered cost and accumulating the potential from left to right. There are three important caveats to state clearly. First, hexagons are treated as independent plants – there is no interaction between them, no shared infrastructure, and no system-level optimisation across the country. Second, demand is fixed per hexagon – this is a screening assumption, not a dispatch-optimised result where demand could be met from multiple locations simultaneously. Third, the production potential estimate depends on the plant_capacity parameter, which you set in the code and which reflects assumptions about how intensively the eligible land is used. This approach is standard for policy-oriented screening analysis and produces results that are directly useful for investment prioritisation. More sophisticated approaches exist – including finer resolution hexagons, dynamic capacity scaling, and system integration models – but for the purpose of this course, and for most policy applications, this methodology is appropriate and well-established.

## Slide 18: Building the supply curve
notebook — supply curve
# ── filter one demand centre ─────────────────
dc = "Odessa"
df = df_cost[df_cost["demand_centre"] == dc].copy()
# ── drop null hexagons ────────────────────────
df = df.dropna(subset=["total_cost"])
# ── production potential per hexagon ─────────
# eligible_area [km²] × plant_capacity [t/km²/yr]
plant_capacity = 1000 # t H₂ / km² / yr — adjust
df["potential"] = df["eligible_area"] * plant_capacity
# ── sort by cost and accumulate ───────────────
df_sorted = df.sort_values("total_cost").reset_index()
df_sorted["cum_potential"] = (
df_sorted["potential"].cumsum() / 1e6 # → Mt/yr
)
# ── plot ──────────────────────────────────────
fig, ax = plt.subplots(figsize=(8, 5))
ax.step(
df_sorted["cum_potential"],
df_sorted["total_cost"],
where="post",
color="#1E3A6E",
linewidth=1.8,
label="Supply curve")
# ── reference price line ──────────────────────
ref_price = None # ← set your own (e.g. 6.0)
if ref_price:
ax.axhline(
ref_price,
color="red",
linestyle="--",
linewidth=1.2,
label=f"Reference: {ref_price} €/kg")
ax.set_xlabel("Cumulative production potential [Mt H₂/yr]")
ax.set_ylabel("Delivered cost [€/kg]")
ax.set_title(f"Supply cost curve — {dc} · hydrogen · 2023")
ax.legend()
ax.grid(True, alpha=0.3)
plt.tight_layout()
plt.savefig(f"plots/supply_curve_{dc}.png", dpi=150)
plt.show()
In the example, the LCOH goes from approximately 6 to over 16 €/kg. The figure is illustrative, and it does not represent any real estimated case.
The flat early section = large volume available at low cost near the demand point.
The steep rise at the right = marginal hexagons far from the demand point with limited eligible area.
Volume is a land-based potential estimate, not the modelled demand (see slide 17).
Notes: This slide shows the complete Python code for building the supply curve, which you can copy and paste directly into your notebook. The code has five logical sections. First, filter to a single demand centre – in this example Odessa – so that you are plotting one curve for one delivery point. Second, drop null hexagons: these are locations where the optimisation was infeasible, either because eligible land was insufficient or because the cost was unconstrained. Third, calculate production potential per hexagon by multiplying the eligible area in square kilometres by a plant capacity parameter in tonnes of hydrogen per square kilometre per year. The value of one thousand used here is illustrative – adjust it to reflect the technology scale you are modelling. Fourth, sort by total cost and compute the cumulative potential in megatonnes per year using cumsum. And fifth, plot the step curve using plt.step with the where equals post option, which draws each step at the right edge of the hexagon's potential – the correct convention for a supply curve. The optional reference price line is drawn as a horizontal dashed line using axhline. Set ref_price to your chosen value – for example a policy target or a competing fuel cost – and the code will add it automatically. The example in the slide shows a curve running from approximately six to over sixteen euros per kilogram. This is illustrative and does not represent any specific real case. The flat section at the left represents the large volume available at low cost in hexagons near the demand point with good renewable resources. The steep rise at the right represents marginal hexagons far from Odessa with limited eligible area – where each additional unit of production becomes significantly more expensive.

## Slide 19
Loading and inspecting outputs
Reading heatmaps
Cost breakdown analysis
Supply cost curves
Wrap up
  Summary and next class overview
Table of Contents
Notes: We are in the final section of the lesson.

## Slide 20: Lesson 5 done! What is next:
20
Loading and inspecting outputs Sanity checks, geopandas, demand centre filter.
Reading heatmaps Spatial gradients, drivers, cross-country comparison.
Cost breakdown analysis Component maps, stacked bars.
Supply cost curves Methodology, construction in Python, policy.
Now you can read and build the core outputs. Lesson 6 covers advanced modelling options that extend what Geo-X can do.
Add technologies (generation – storage)
Demand flexibility
Well done! See you in the last lesson, Lesson 6, of the course.
What you’ve set up so far:
Lesson 6 coming up
Note: Figures and graphics throughout this course were produced by the authors, generated either through custom Python code or with the assistance of Claude AI.
Notes: Let us take stock of what this lesson has covered and look ahead to the final lesson of the course. You have learned four analytical skills. First, loading and inspecting outputs: using geopandas to read the GeoJSON files, running the three sanity checks on shape, columns, and cost range, and filtering to a specific demand centre. Second, reading heatmaps: understanding the visualisation design decisions, recognising the spatial correlations between LCOH and renewable resource maps, understanding the storage-variability relationship, and knowing what the heatmap cannot tell you. Third, cost breakdown analysis: producing the two-by-two component maps, interpreting the spatial pattern of each component, and using the stacked bar chart to summarise cost composition for the most competitive zones. And fourth, supply cost curves: understanding what the curve represents conceptually, knowing the methodology and its assumptions honestly, and building it in Python from your own Geo-X outputs. Lesson 6 is the final lesson of the course. Having covered interpretation, Lesson 6 turns to advanced modelling options that extend what Geo-X can do: adding new generation technologies such as geothermal or nuclear, incorporating storage alternatives, and exploring demand-side flexibility. See you there.

## Slide 21: Thank you
www.climatecompatiblegrowth.com
Notes: Thank you for completing Lesson 5 of the Geo-X training course. You can now move from raw model outputs to policy-relevant analysis. In Lesson 6 we explore the advanced options that allow you to extend and customise Geo-X beyond the defaults.