## Slide 1: Geo-X training course
Lesson 6: Advanced options
Notes: Welcome to Lesson 6 of the Geo-X training course: Advanced Options. This is the final lesson of the course. You can already install Geo-X, prepare inputs, run the model, and interpret the results. This lesson extends those skills by introducing three modelling features that reflect real-world complexity: a generic dispatchable generator that acts as a proxy for a power purchase agreement or an existing low-carbon fleet, flexible demand that relaxes the rigid hourly production constraint, and an approximation of salt cavern storage for geologically eligible locations. All three features live in the feature/flexible_demand branch of the Geo-X repository, and all three are activated through parameter changes only (no new code is required).

## Slide 2: Learning outcomes
By the end of this lesson, you will:
Check out the feature/flexible_demand branch and understand how it extends the main branch
Configure and run a generic generator to represent a power purchase agreement or existing low-carbon fleet
Configure flexible demand using the three h2_demand_flex parameters and interpret its effect on storage costs
Approximate salt cavern storage by running a separate scenario over geologically eligible hexagons with salt cavern CAPEX in stores.csv , and quantify the competitive advantage this creates.
Compare advanced scenario results against a baseline using the tools from Lesson 5.
2
Notes: Here are the five learning outcomes for this lesson. By the end you will be able to check out the feature/flexible_demand branch and understand how it extends the main branch. You will be able to configure and run a generic generator scenario to represent a power purchase agreement or an existing low-carbon fleet. You will be able to configure flexible demand using the three h2_demand_flex parameters and explain its effect on storage costs. You will be able to implement the salt cavern approximation by modifying storage dot csv CAPEX for geologically eligible hexagons. And you will be able to compare advanced scenario results against a baseline using the analytical tools from Lesson 5. These five outcomes build directly on every lesson that came before.

## Slide 3
Getting the feature branch
Generic generator: The PPA proxy.
Flexible demand
Salt caverns
Wrap up
  What feature does the branch add
  Checking out the branch
Table of Contents
Notes: Here is the structure of this lesson. We begin by getting the feature branch and understanding what it adds. We then go through each of the three advanced features in turn: first the generic generator, then flexible demand, then salt cavern storage. Each section follows the same pattern: what it is conceptually, how to configure it, what changes in the results, and why it matters for policy. We close with a course summary and citation information.

## Slide 4: What features does the branch add?
4
New in this branch | What to modify | What it does
generic_generator Dispatchable source. It acts as a proxy for a PPA or existing grid-connected assets. | config.yaml Modifying generic_generator: marginal_cost: [€/MWh] | Adds a generator that can dispatch at any hour (unlike solar and wind). Capacity drawn from hexagon attributes (e.g. hydro + nuclear for low-carbon existing assets). Marginal cost set by the analyst in €/MWh.
h2_demand_flex Demand flexibility can reduce the need for storage, and therefore, lower LCOH. | config.yaml h2_demand_flex: True h2_demand_flex_hours: [hours] h2_demand_flex_power_fraction: [0–1] h2_demand_flex_energy_fraction: [0–1] | Allows demand to shift within a time window (the electrolyser ramps up when renewables peak and down otherwise). Reduces storage requirements and lowers LCOH.
salt cavern approximation Geological advantage that reduces the storage CAPEX. | stores.csv CAPEX reduced for eligible hexagons (salt_cavern_eligible field in the GeoJSON) | Where geology permits, H₂ can be stored in salt caverns at far lower CAPEX than compressed tanks. Flagged in Lesson 3, now applied.
Three extensions to the baseline – all activated through parameter changes only.
Notes: This slide gives you the map for the whole lesson – a compact overview of the three extensions introduced in the feature/flexible_demand branch. The first is the generic generator block in config.yaml. This adds a dispatchable electricity source to each hexagon, with capacity set from the hexagon GeoJSON attributes and marginal cost set by the analyst. It acts as a proxy for a power purchase agreement, a grid connection, or legacy low-carbon generation. The second is the h2_demand_flex flags, also in config.yaml. These relax the rigid hourly demand constraint, allowing the optimiser to shift production within a defined time window. Economically, this is equivalent to giving the system a free virtual storage buffer on the demand side. The third is the salt cavern approximation, implemented through stores.csv. For hexagons where salt cavern geology is available, the hydrogen storage CAPEX is reduced to reflect cavern economics rather than compressed tank costs. The key message of this slide: all three features are activated through parameter changes only. You do not need to modify any Python code: you only edit the files you already know from Lessons 3 and 4.

## Slide 5: Checking out the feature branch
5
Step 1 — Get the branch from the CCG upstream repo
terminal — from the root of your cloned Geo-X repo
git fetch upstream
git checkout -b feature/flexible_demand upstream/feature/flexible_demand
Step 2 — Create your own analysis branch off it — do not work directly on feature/flexible_demand
terminal
git checkout -b my-analysis/country-flex
# now on your branch, based on feature/flexible_demand
# edit config.yaml, run map_all, commit — same workflow as Lesson 2
Branch structure
CCG/feature/flexible_demand
your fork / feature branch
my-analysis/[case]
your work lives here
edit config.yaml, run map_all, commit
— same Lesson 2 workflow
Keeps CCG's feature/flexible demand clean. Your changes don't overwrite the base.
Your config edits stay in your fork, traceable and comparable across scenarios.
Easy to contribute improvements back upstream via Pull Request.
Same habit as Lesson 2.
Notes: Getting the feature branch follows the same Git workflow you practised in Lesson 2, with one additional step. First, fetch the latest branches from the upstream CCG repository using git fetch upstream. Then create a local tracking branch using git checkout -b feature/flexible_demand upstream/feature/flexible_demand. You are now on the CCG feature branch. But, and this is important, do not work directly on this branch. The discipline from Lesson 2 applies here too: immediately create your own analysis branch off it using git checkout -b followed by a descriptive name for your case study. Your config edits, your model runs, and your results all go into your branch, not into feature/flexible_demand. This keeps the CCG branch clean, makes your changes traceable across scenarios, and makes it easy to contribute improvements back upstream via a pull request when you are ready. The branch structure shown on this slide (CCG feature branch as the base, your analysis branch sitting on top) is exactly the same pattern as Lesson 2. The only difference is the starting point.
Create upstream remote:
git remote add upstream \ https://github.com/ClimateCompatibleGrowth/Geo-X.git
# the command is run once
git fetch upstream git switch -c my-analysis/country-flex \ upstream/feature/flexible_demand

## Slide 6
Getting the feature branch
Generic generator: The PPA proxy
Flexible demand
Salt caverns
Wrap up
  What the generic generator represents
  Configuring the generic generator
  What changes in the results and policy relevance
Table of Contents
Notes: We now go into the first advanced feature: the generic generator. This section covers what it represents conceptually, how to configure it, what it changes in the results, and its policy relevance.

## Slide 7: What the generic generator represents
7
What it is:
A dispatchable electricity source added to every hexagon. Unlike solar and wind, it can generate at any hour. Thus, the optimiser can call on it whenever renewable output is insufficient.
p_nom [MW]
Installed capacity per hexagon, set by the modeller in the GeoJSON attributes.
marginal_cost [€/MWh]
The price at which that electricity is available to the optimiser. Set in config.yaml. This is one value for all hexagons.
How the optimiser decides:
If marginal cost is lower than the LCOE of solar PV, wind turbines and storage, then the generic generator will be preferred by the optimiser.
If marginal cost is slightly* higher than the LCOE of renewables, then the optimiser can incorporate the generic generator, but the aim is to reduce the amount of storage facilities needed.
In that case, the relevant comparison is between the cost of energy from the generic generator and the cost of the storage capacity it displaces.
(*) Slightly gives an account about how comparable are both costs.
How to interpret the marginal cost:
PPA contract price: the fixed price the producer pays a generator under a power purchase agreement.
Local grid tariff: Retail or industrial electricity tariff in the hexagon’s region.
Shadow cost/legacy generation: Implicit cost of existing hydro or nuclear generation.
The analytical applications:
Test different PPA prices to verify break-even points for storage installation.
Analyse real-world electricity prices in different regions.
Capture opportunity cost of using low-carbon assets for commodity production.
Notes: The generic generator adds a dispatchable electricity source to every hexagon in the model. Unlike solar and wind, which are constrained by weather availability and can only generate when the resource is there, the generic generator can dispatch at any hour, the optimiser can call on it whenever renewable output is insufficient to maintain production. It has two key parameters. The first is p_nom – the installed capacity in megawatts per hexagon. This is read from the hexagon GeoJSON attributes, not set in config.yaml. For Ukraine, a natural interpretation is to set p_nom equal to the combined capacity of low-carbon dispatchable assets in or near each hexagon – For instance, hydropower and nuclear. In general, the analyst decides what capacity to assign based on the generation assets they want to model. The second parameter is marginal cost – the price in euros per megawatt-hour at which that electricity is available to the optimiser. This is set globally in config.yaml and applies to all hexagons. The optimiser's decision logic is straightforward: if the marginal cost of the generic generator is lower than the combined cost of renewable generation and storage to maintain the same output, the generator will be dispatched. If it is slightly higher, the generator may still be used to replace storage rather than renewables – because buying a little expensive electricity at the right moment can be cheaper than building storage capacity. If it is much higher, the optimiser will not use it at all. This is the break-even logic that makes the generic generator analytically powerful: by sweeping across marginal cost values, you can map out exactly where and when grid access adds value.

## Slide 8: Configuring the generic generator
8
config.yaml: a segment to modify
config.yaml
generators_dict: {'solar' : [], 'wind' : [], 'existing' : []}
gen_capacity:
solar: 1
wind: 4
existing: 1
# Generic dispatchable generator (existing fleet):
# p_nom per hexagon = hydro + nuclear from data/{country}/hex_final_{country}.geojson
generic_generator:
marginal_cost: 60
‘Existing’ generation is added in the generators_dict, adding an alternative in the portfolio of the optimiser.
p_nom draws from the sum of hydro + nuclear in the data of the country. p_nom is read from the hexagon GeoJSON, not set in config.yaml.
marginal_cost considers the cost of the energy in €/MWh of the electricity consumed.
Considering a very high value of marginal_cost (for example, 500€/MWh) results in no participation of the generic generator. Effectively, this case can be considered as the base case.
Considering a realistic value of marginal cost for PPA results in the generic generator displacing both renewable generation and storage facilities.
Considering a very low value of marginal cost for PPA results in the generic generator displacing a significant amount of renewables and storage.
Notes: This slide shows the exact lines to add or modify in config.yaml to activate the generic generator. Two changes are needed. First, add 'existing' to generators_dict alongside solar and wind. This tells the optimiser that a third generator type is available. Second, add the gen_capacity entry for existing – set to 1 in the example, which acts as a scaling factor – and add the generic_generator block with a marginal_cost value. The example uses 60 euros per megawatt-hour, which is broadly representative of a competitive power purchase agreement price in a European context. Remember that p_nom is not set here – it is read from the hydro and nuclear attributes of the hexagon GeoJSON file. As a practical guide on setting marginal cost: a very high value such as 500 euros per megawatt-hour effectively disables the generator and reproduces the off-grid baseline. A realistic PPA price in the range of 50 to 80 euros per megawatt-hour gives a scenario where the generator competes with storage. A very low value close to zero gives an optimistic upper-bound scenario where grid electricity is essentially free – useful as a sensitivity bound to understand the maximum possible impact of grid access on LCOH.

## Slide 9: What changes in the result
9
Effect on storage and spatial pattern:
Storage requirements fall when generic generators are included. Even for high marginal cost (140 in the example), the generic generator provides the flexibility to couple variable energy resources with hydrogen production.
For low marginal cost, the generic generator displaces variable energy resource generators.
For high marginal cost, the generic generator displaces the storage
Spatial pattern may be shifted, considering storage requirement changes, possibly changing the relative cost of each hexagon.
The image shows an illustrative example of the LCOH considering a generic generator with different marginal costs (60, 100 and 140 €/MWh).
Policy relevance
This approach allows quantification of the role of the network in commodity production, as a source of flexibility for coupling variable energy resources and demand.
It can measure the potential impact of the power system on the levelised cost of production, with electricity costs in a specific country.
Notes: What changes in the results when you add a generic generator? The key finding, shown in the illustrative example on this slide, is that storage requirements fall even at relatively high marginal costs. At 140 euros per megawatt-hour – well above competitive renewable LCOE – the generic generator is still dispatched in the optimiser because it provides flexibility at the margins: filling in the gaps in renewable output that would otherwise require expensive storage capacity. At lower marginal costs, such as 60 euros per megawatt-hour, the generator begins displacing renewable generation directly as well, because grid electricity is now cheaper than building additional solar or wind. The spatial pattern of results also changes: hexagons closer to existing low-carbon generation capacity benefit more, which may shift the ranking of the most competitive production locations relative to the purely off-grid baseline. The policy relevance is clear. This feature allows Geo-X to quantify the role of the electricity network as a source of flexibility for coupling variable renewables with hydrogen production. It can measure how much a specific grid electricity price – or a specific PPA contract – affects the levelised cost of production across the entire country, and where that effect is largest.

## Slide 10
Getting the feature branch
Generic generator: The PPA proxy.
Flexible demand
Salt caverns
Wrap up
  What flexible demand means
  Three parameters
  What changes in the results and policy relevance
Table of Contents
Notes: We now move to the second advanced feature: flexible demand. This section covers the concept, the three parameters, the effect on results, and the policy relevance.

## Slide 11: What does flexible demand mean?
11
Baseline – rigid hourly demand
The hydrogen plant must produce at a constant rate, uncorrelated with renewable availability.
To keep a constant output, the system requires storage facilities. It is important to consider the loss of efficiency associated with storage systems.
Who faces rigid demand constraints:
Pipelines with continuous flow requirements.
Industrial processes with no buffer vessels.
Port offtakers with fixed ship loading schedules.
With flexible demand
The hydrogen plant can vary output over a defined window, as long as it meets total demand over that period.
Economically, a “free storage” buffer on the demand side. Thus, the buyer absorbs timing variability, removing the plant's need to smooth its own output. There are lower losses for storage systems.
Who can offer demand flexibility:
Buyers with large H₂ storage tanks on-site.
Industrial processes with buffer vessels (ammonia, refineries).
Port terminals with holding capacity before ship loading.
In Geo-X, set h2_demand_flex: True in config.yaml. The optimiser gains a free intra-period buffer and will dispatch the electrolyser when renewables are cheapest.
t
t+1
t+2
H charged in storage
eta*H discharged from storage
Fixed demand
t
t+1
t+2
Variable demand
H
H
Notes: The baseline Geo-X model applies a rigid demand constraint: the hydrogen plant must produce at a constant rate at every hour of the year, regardless of when renewable energy is available. This is a conservative assumption. To maintain constant output, the system must invest in storage to smooth the mismatch between variable supply and fixed demand, and storage carries efficiency losses on every cycle. The diagram on the left of this slide illustrates this: hydrogen is charged into storage in one period and discharged (with an efficiency loss) in the next, simply to maintain a flat demand profile. Flexible demand changes this. Instead of meeting demand at every individual hour, the plant only needs to meet total demand over a defined rolling window. Within that window, the optimiser is free to ramp the electrolyser up when renewables are abundant and down when they are scarce. The diagram on the right shows the result: production follows the renewable resource rather than fighting it. Economically, this is equivalent to a free storage buffer on the demand side (the buyer absorbs the timing variability), removing the need for the plant to invest in as much storage. Who can offer this flexibility? Buyers with large on-site hydrogen storage tanks, industrial processes with buffer vessels such as ammonia plants or refineries, and port terminals with holding capacity before ship loading. Who cannot? Pipeline networks with continuous flow requirements, industrial processes with no buffer, and port offtakers with fixed ship loading schedules. Understanding which buyers can offer flexibility, and what that flexibility is worth, is one of the most practically useful things Geo-X can now quantify.

## Slide 12: The three flexibility parameters
12
config.yaml — flexible demand parameters
h2_demand_flex:
True
# enable/disable
h2_demand_flex_hours:
168
# flexibility window — 168 = 1 week
h2_demand_flex_power_fraction:
0
# fraction of power demand that can be shifted
h2_demand_flex_energy_fraction:
1.0
# fraction of total energy demand that can be shifted
h2_demand_flex_hours | h2_demand_flex_power_fraction | h2_demand_flex_energy_fraction
The number of hours the optimiser can defer the commodity production. | The maximum fraction of the power demand (MW) that can be considered as flexible. | The maximum energy demand (MWh) that can be shifted.
24h reflects a daily flexibility; 168h allows shifts within a week; 720h energy shifts during a month. | A value of 1 means that the plant can be completely shut down during scarce renewable availability. A value of 0 means that no flexibility is possible. | A value of 1 means that 100% of the demand can be shifted. A value of 0 means that no energy can be shifted.
In practice, demand side flexibility can be understood as a virtual storage for free whose power and energy capacity is controlled by the 3 parameters.
Notes: The enable flag plus three config.yaml parameters for flexible demand give fine-grained control over how much flexibility is modelled. Firstly, h2_demand_flex simply enables or disables the feature. Set it to True to activate. The first parameter is h2_demand_flex_hours, which defines the length of the flexibility window in hours. A value of 24 gives daily flexibility – the optimiser can shift production within each day. A value of 168, equivalent to one week, allows weekly shifts. A value of 720 allows monthly shifts – approximating seasonal flexibility. The longer the window, the more freedom the optimiser has to follow the renewable resource, and the greater the potential storage savings. The second is h2_demand_flex_power_fraction, which sets the maximum fraction of hourly power demand that can be shifted. A value of 1 means the plant can shut down completely during periods of poor resource availability; a value of 0 means no hourly flexibility. A value of 0.3 allows up to 30 percent of each hour's demand to be moved. The third is h2_demand_flex_energy_fraction, the maximum fraction of total energy demand that can be shifted across the window – 1.0 would allow all of it to move, though in practice no more than about half the energy in a period can be shifted. Together these define a virtual storage buffer: its energy capacity is set by the hours parameter, its power capacity by the power fraction. The key practical insight: in a solar-heavy environment, setting h2_demand_flex to True with a one-week window and 1.0 power fraction can produce substantial storage cost reductions at no additional capital cost – because the flexibility already exists on the demand side.

## Slide 13: What changes in the result and policy relevance
13
What changes in the results:
Solar-heavy regions: larger expected effect | Wind-rich regions: lower expected effect | Recommended test
Solar PV requires storage to keep the production constant 24/7. In this case, a better coupling between demand and supply could reduce the needed storage investment. | Wind availability can be less variable than solar PV. As such, the storage needed for wind-dominant zones would be comparatively lower. Thus, the flexible demand may have lower relevance. | Compare in which hexagons the usage of flexible demand had a higher impact on the levelised cost of production.
Policy relevance:
When flexible demand makes sense
Some physicochemical processes are inherently inflexible. For instance, ammonia production requires the use of the Haber-Bosch process that does not offer the same flexibility as electrolysers.
Some offtakers manage industrial processes where they can adjust the commodity consumption (e.g. hydrogen), leveraging thermal inertia or other capabilities.
Some consumers may have large tanks (for example, port terminals with buffer vessels before ship loading).
What Geo-X adds to the analysis
Spatial quantification where flexibility is most valuable, identifying which locations benefit most from flexibility.
It can contribute to the contract design, identifying the impact of the flexible parameters as a negotiation parameter.
Notes: What changes in the results when flexible demand is activated? The effect is strongest in solar-heavy regions, where rigid demand previously forced large battery investments to smooth the day-night cycle. With flexible demand, the electrolyser can simply run during daylight hours and rest at night – eliminating much of the storage requirement. In wind-rich regions the effect is smaller, because wind output is already smoother across hours, so less storage was needed in the baseline to begin with. The recommended scenario pair is straightforward: run with h2_demand_flex set to False – which is the baseline – then run again with h2_demand_flex set to True and h2_demand_flex_hours set to 168. Compare the storage cost component maps from the two runs using the tools from Lesson 5. The hexagons where the cost reduction is largest are those where the buyer's flexibility is most valuable. On the policy side, this analysis has direct implications for contract design. Not all buyers can offer flexibility – some physicochemical processes are inherently rigid. Haber-Bosch ammonia synthesis, for instance, operates most efficiently at steady state and offers limited flexibility compared to an electrolyser. But buyers with large tanks, or those who can adjust hydrogen consumption in response to delivery timing, may be able to offer meaningful flexibility at very low cost. Geo-X gives you the spatial quantification of where that flexibility matters most – which turns it from a qualitative contractual discussion into a quantitative negotiation parameter.

## Slide 14
Getting the feature branch
Generic generator: The PPA proxy.
Flexible demand
Salt caverns
Wrap up
  What salt caverns offer and availability
  Implementing the approximations in three steps
  Expected results and policy relevance
Table of Contents
Notes: We now move to the third advanced feature: salt cavern storage. This is the most geographically specific of the three features, because it depends on local geology rather than a universal parameter choice.

## Slide 15: What are salt caverns?
15
What it is
Underground cavities leached from thick salt deposits (evaporites). Used for decades to store natural gas and compressed air. Now increasingly considered for hydrogen at scale.
Where they are available and how to adjust the model
Geological requirements: Thick evaporite salt deposits. Those locations are not necessarily correlated with good renewable conditions.
In Geo-X, one alternative to model the usage of salt caverns is executing a separate model run considering those hexagons where salt caverns are available.
For those hexagons, the cost of hydrogen storage can be modified considering the techno-economic parameters associated with salt caverns.
Attribute | Comments
Cost per MWh | The CAPEX associated with salt caverns is more than an order of magnitude cheaper than compressed tanks
Scale | Compressed tanks offer a lower amount of storage (around MWh-GWh) than salt caverns (Around GWh-TWh).
Flexibility | Compressed tanks can do 120 cycles per year, whereas salt caverns can do around 10 cycles.
Griñán, G. G., & Gómez-Acebo, T. (2026). Techno-economic analysis of hydrogen storage options using a reproducible software model. International Journal of Hydrogen Energy, 258, 156618.
–> One important consideration is that Geo-X assumes production and storage of hydrogen within the same hexagon. In practice, storage of hydrogen can be localised in a region where salt caverns are available, while production is in another.
Notes: Salt caverns are underground cavities leached from thick evaporite salt deposits. They have been used for decades to store natural gas and compressed air at industrial scale, and they are now increasingly considered for hydrogen storage. The economic advantage over above-ground compressed tank storage is significant: on a cost-per-megawatt-hour basis, salt caverns are roughly one order of magnitude cheaper than compressed tanks. The table on this slide summarises the key differences. On cost per megawatt-hour, compressed tanks are far more expensive. On scale, compressed tanks offer storage in the megawatt-hour to gigawatt-hour range, while salt caverns can operate at the gigawatt-hour to terawatt-hour scale. On flexibility, compressed tanks support around 120 charge-discharge cycles per year, while salt caverns typically support around ten cycles, which means caverns are suited to seasonal storage rather than daily or weekly balancing. This last point is important for how you use the salt cavern approximation in Geo-X: caverns provide cheap bulk seasonal storage, not fast-cycling flexibility. The other important modelling consideration is that Geo-X assumes production and storage occur within the same hexagon. In practice, a production site and a salt cavern may be in different locations – the hydrogen produced in one hexagon could be transported to a cavern in another for seasonal storage before onward distribution. Capturing that spatial separation would require a more complex model. The Geo-X approximation – reducing storage CAPEX for hexagons that overlie cavern geology – is appropriate for screening purposes but should be stated as an assumption when reporting results.

## Slide 16: Implementing salt caverns in Geo-X: 3-step approximation
16
1. Identify eligible locations
2. Apply differentiated techno-economic parameters
3. Quantify the spatial benefit
Extract hexagons where salt caverns are potentially available. Create a new GeoJSON with those hexagons.
Thus, Geo-X will be able to execute this subset of hexagons.
Modify the techno-economic parameters in stores.csv (CAPEX, efficiency, cycles) to reflect salt cavern characteristics.
As a result, the hexagon subset will have a differentiated set of parameters to evaluate salt caverns.
Compare the heatmaps and LCOH in both cases (with salt caverns and compressed hydrogen tanks).
An expected result is that the salt caverns will have a higher impact where the renewable potential and need for storage facilities are greatest.
Notes: Implementing the salt cavern approximation in Geo-X follows three steps. Step one is identifying the eligible hexagons. This is done externally, in Python or QGIS, using a geological survey layer showing salt basin extent. You load the salt basin polygon, intersect it with your hex_final GeoJSON, and flag the overlapping hexagons. You then create a new GeoJSON file containing only those hexagons – this is the subset that Geo-X will run with differentiated storage parameters. Step two is applying the differentiated techno-economic parameters. Open parameters/basic_h2_plant/stores.csv in the parameters folder and modify the capital cost entry for the hydrogen storage component – reducing it from the compressed tank value to a value representative of salt cavern costs. The specific values to use come from the literature; a good starting point is the reference cited on the previous slide. With this modified stores.csv, running Geo-X on the eligible hexagon subset gives you cost estimates that reflect cavern economics rather than tank economics. Step three is quantifying the spatial benefit by comparing results. Run the baseline scenario – all hexagons, standard compressed tank CAPEX. Then run the cavern scenario – eligible hexagon subset, reduced CAPEX. The difference in LCOH between the two runs, mapped spatially, reveals which production locations gain the most from cavern access. As a general expectation: the benefit is largest where renewable resources are variable and storage costs were already a significant share of total LCOH in the baseline – solar-heavy regions in particular.

## Slide 17: Possible results and policy relevance
17
Geology could overturn the renewable resource map
Access to lower-cost storage can reduce the storage penalty associated with variable solar and wind generation.
Including potential cavern access may change the ranking of the most competitive production locations.
High renewables, no cavern access
Cavern-enabled,
lower storage cost
Possible policy consequences
Policy makers: combine geological storage surveys with renewable resource mapping in national green hydrogen assessments.
Investors: treat overlap with suitable salt formations as material to site selection and project economics.
Notes: This slide presents the key policy insight from the salt cavern analysis. Geology can overturn the renewable resource map. A location with moderately good renewable resources but access to cheap cavern storage may be more competitive than a location with excellent resources but no suitable geology. This is a result that a purely resource-based assessment – looking only at solar irradiation and wind speed – would miss entirely. The two-by-two comparison on this slide illustrates the logic: a high-renewables location with no cavern access versus a cavern-enabled location with lower renewable potential. Depending on the magnitude of the storage cost reduction, the cavern-enabled location may end up with a lower total LCOH. For policymakers, the implication is that geological storage surveys should be part of any national green hydrogen assessment, sitting alongside renewable resource mapping as a standard input rather than an afterthought. For investors, the overlap between a candidate site and suitable salt formations is material to project economics – it is the kind of information that should appear in site selection criteria alongside grid access, water availability, and distance to demand.

## Slide 18
Getting the feature branch
Generic generator: The PPA proxy.
Flexible demand
Salt caverns
Wrap up
  General summary
  Contact
Table of Contents
Notes: We are now in the final section of the course.

## Slide 19: General summary
19
Lessons | Core skills
1 Introduction to Geo-X | Frame Geo-X applications, data needs, and research or policy questions.
2 Software setup | Install the software, navigate the repository, and validate the data-prep workflow.
3 Data inputs | Define pathways, demand locations, and techno-economic parameter assumptions.
4 Running the model | Configure and run scenarios, troubleshoot, and export CSV, GeoJSON, and heatmaps.
5 Interpreting results | Interpret spatial patterns, LCOH/LCOA breakdowns, and cumulative supply curves.
6 Advanced options | Extend the model with a dispatchable generator, flexible demand, and salt cavern storage.
You have finished the course – let’s have a look at what we have learnt:
Notes: This table summarises the six lessons and the core skill each one gave you. Lesson 1 gave you the conceptual foundation: what Geo-X is, how it differs from other tools, and the kinds of research and policy questions it can address. Lesson 2 gave you the technical foundation: installing the software, navigating the repository, and establishing the Git workflow you have used throughout the course. Lesson 3 gave you data literacy: defining production pathways, setting demand locations, and configuring the techno-economic parameters that drive the model. Lesson 4 gave you operational skill: running the full Snakemake workflow, troubleshooting errors, and designing multiple scenarios. Lesson 5 gave you analytical skill: interpreting cost heatmaps, decomposing LCOH into its components, and building cumulative supply cost curves. And this lesson, Lesson 6, extended those skills to three advanced modelling configurations that reflect real-world policy questions. Together, these six lessons give you the full Geo-X workflow, from data preparation to advanced scenario analysis. You are now equipped to apply this tool to your own country, your own commodity, and your own policy question.

## Slide 20: Citation for Geo-X model
20
Please cite this work as:
Sanchez-Lopez, M., Naqvi, S., Leonard, A., Schirren, L., & Hirmer, S. (2026). Geo-X: Generalised geospatial software for production of green commodities. SoftwareX, 34, 102712.
Note: Figures and graphics throughout this course were produced by the authors, generated either through custom Python code or with the assistance of Claude AI.
Notes: This slide gives you the citation and contact information for Geo-X. When you use the tool in your own research or policy work, please cite the SoftwareX paper: Sanchez-Lopez, M., Naqvi, S., Leonard, A., Schirren, L., and Hirmer, S., 2026, Geo-X: Generalised geospatial software for production of green commodities, SoftwareX, volume 34, article 102712. The CCG website is also a resource for case studies, working papers, and news about tool developments.

## Slide 21: Thank you
www.climatecompatiblegrowth.com
Notes: Thank you for completing the Geo-X training course. Over six lessons you have built a complete set of skills: the conceptual framework, the software environment, data preparation, model execution, results interpretation, and advanced modelling options. We hope you will put these tools to work in your own research and policy contexts. Good luck, and we look forward to seeing what you build with Geo-X.